## Slide 1: Identification and Representation of Homotopy Classes of Trajectories for Search-based Path Planning in 3D
Subhrajit Bhattacharya
Maxim Likhachev
Vijay Kumar
<number>
University of Pennsylvania
GRASP
LABORATORY

## Slide 2: Homotopy Classes in 3 Dimensional Configuration Spaces
<number>
Trajectories in different homotopy classes
Trajectories in same
homotopy class
initial
final
?
?
?
?
Path prediction of dynamic agents in environment with dynamic obstacles
e.g. in tracking dynamic agents through multiple occlusions
J. Shi, et al.
Motivational Examples:
Planning trajectories in specific homotopy class (e.g. trajectory through a window)
D. Mellinger, et al.

## Slide 3: Contributions
Design an efficient representation of homotopy classes of trajectories.
Use the representation for :
  Finding least cost paths with homotopy class constraints (solve the constrained optimization problem).
  Explore different homotopy classes in a 3D configuration space.
Integrate the representation with graph-search based planning algorithms.
  Plan for optimal cost paths, for arbitrary cost function (not necessarily Euclidean distances), arbitrary discretization schemes (Uniform, unstructured, triangulation, visibility graph, etc.) using any graph search algorithms (Dijkstra’s, A*, D*, ARA*, etc.).
<number>

## Slide 4: Homotopy Classes in Two Dimensional Space (previous work: AAAI’10)
<number>
Re
Im
ζ1
ζ2
ζ3
τ1
τ2
τ3
“Representative points” inside obstacles.
start
goal
Can be used for graph-search based planning with homotopy class constraints.
Homotopy class exploration in a large environment (1000x1000 discretized)
Planning with homotopy class constraints
(visibility constraint)
Key ideas:
1. Represent the configuration space by a complex plane
2. Construct an analytic function with singularties at “representative points”.
3. Leverage Cauchy Integral and Residue Theorems to design an additive homotopy class invariant.
Applications
& examples:

## Slide 5: Three Dimensional Spaces – Exploit Theorems from Electromagnetism
<number>
Ampere’s Law
B: Magnetic field vector
μ0: Magnetic constant (can be chosen as 1 with proper choice of units)
Biot-Savart’s Law

## Slide 6: Extraction of skeletons of 3D obstacles
<number>
Arbitrary obstacles
Close unbounded obstacles
Virtually decompose
genus > 1 obstacles
A simple homotopy inducing obstacle (SHIO)
Construct skeleton of a SHIO and model
that as a current carrying conductor

## Slide 7: h-Signature
<number>
Virtual Magnetic Field due to ith SHIO
h-signature of trajectory τ
where,
We can use h-signatures to identify homotopy classes of trajectories

## Slide 8: h-signature augmented graph
<number>
Given the discretization graph laid upon the environment, we construct,
v in G
{v, H(zs→z)} in G H
H
H
H
such that, each node in G, is augmented with a h-signature in GH , so that nodes are distinguished by homotopy class of path taken to reach them
Definition is similar to that of L-augmented graph used for the 2D case (AAAI’10).
More details at the poster!
Insight into topology of the augmented graph (the 2-D case):

## Slide 9: Results
<number>
Exploration of 4 homotopy classes in presence of 2 SHIOs:
Exploration of 4 homotopy classes
in presence of 4 SHIOs:
Planning in X-Y-Time configuration space:
Planning in X-Y-Z configuration space:
More results at the poster

## Slide 10
More at the poster:
More results
Discussion on computational efficiency
Homotopy vs homology – what it means for robotics applications?
<number>
Thank you!
Please stop by at the poster.