## Slide 1
The Littledog
Quadruped Robot
Manufactured by
Boston Dynamics
The Vicon
Motion Capture System (MOCAP)‏
BB:
Why walk when you can roll on wheels?
Challenges (coming up)‏

## Slide 2
© Boston Dynamics
BB:
Description of legs

## Slide 3
Actuators:
  12 servo motors for controlling the 12 joints of the robot ── that's the only control we have!
MOCAP system:
  Reflective markers on the robot and the terrain boards
  Red LEDs flashing light on the markers
  6 cameras looking down on the terrain and the robot to locate the markers
On-board sensors:
  3-axes force sensor on each leg
  IMU for measuring the orientation and angular speeds of the robot
  Laser range sensor
BB:
How mocap locate the terrains
Obtaining terrain height map
More discussion on the sensors

## Slide 4
Topology of the configuration manifold of a mobile robot
x
y
θ
v
ω
Configuration uniquely defined by:
(x, y, θ)‏
→ 3 dimensional configuration space.
But θ, unlike z,
does not go from -∞ to +∞.
It ranges from -π to +π, with -π ≡ +π.
→ That's the “topology”!
→ We call it a
“configuration manifold”.
Possible directions of motion:
Only v and ω – no side motion possible!
→ Non-holonomic system.
BB:
R, Rn, S, Sn, SO(2), SE(2), SO(3), SE(3) manifolds
What is a manifold?
More discussion on possible directions of motion (tangent space)‏

## Slide 5
Configuration manifold of a quadruped robot
It is 18 dimensional !!
- How?
Constraints:
- Feet, Body cannot penetrate the terrain surface
Assumptions:
- At least 3 feet should touch the ground at any instant
- Statically stable system / quasi-static system
- No slippage at the feet
John William Goodwine, Jr., Control of Stratified Systems with Robotic Applications, Doctoral Thesis, California Institute of Technology (1997).
Subhrajit Bhattacharya, Motion Planning in a Stratified Workspace Manifold of a Quadruped Walking Robot, Technical Report, University of Pennsylvania (2007).
Configuration Manifold characterized by discontinuities and constraints in direction of motion – A Stratified Manifold
Further reading:
BB:
More details on stratified manifolds (simple example)‏
Specific to this robot

## Slide 6
Forward and Inverse Kinematics
Forward Kinematics:
Given θ1 and θ2, find x and y:
x = l1 cos (θ1) + l2 cos (θ2)‏
y = l1 sin (θ1) + l2 sin (θ2)‏
(x, y)‏
θ1
θ2
l1
l2
θ1A
θ2A
θ2B
θ1B
(x, y)‏
Inverse Kinematics:
Given x and y, find θ1 and θ2:
More difficult
Multiple solutions
θ1A = α – β1 ; θ2A = α + β2 → First solution
θ1B = α + β1 ; θ2B = α – β2 → Second solution
where,
α = atan2(y, x)‏
β1 = cos-1(2 l1 / R)‏
β2 = cos-1(2 l2 / R)‏
R = (x2 + y2)1/2
BB:
Details of the calculations
atan2 function

## Slide 7
Forward and Inverse Kinematics in more complex manipulators in 3 dimensions
Forward Kinematics [given (θ1, θ2, θ3) find (x, y, z)]:
Relatively simple
Unique solution
Generally done by making use of “Exponential coordinates” and “homogeneous transformation matrices”
Inverse Kinematics [given (x, y, z) find (θ1, θ2, θ3)]:
Relatively complex
Generally 2 possible solutions
Generally done by making use of “Paden Kahan Subproblems" [Further reading: Richard M. Murray, Zexiang Li, S. Shankar Sastry, A Mathematical Introduction to Robotic Manipulation, CRC Press LLC (1994)]
Each Leg of the Littledog Robot has
3 degrees of freedom,
i.e. 3 independent joints:
- Hip RX (θ1)‏
- Hip RY (θ2)‏
- Knee RY (θ3)‏
The end effector (foot) can reach points (x,y,z) in a limited region of the 3D space called the workspace of the leg.
BB:
PK subproblems 1, 2 & 3
Solving FK and IK for the littledog's legs

## Slide 8
Achieving desired joint angles – the PD controlled servo motors
Note:
When θ = θd, and θ = θd are achieved, τ becomes zero,
Else the torque is such that θ is driven towards θd, and θ is driven towards θd !
I (current)‏
Command of desired
θd and θd
Reading from sensors
of θ and θ achieved
The controller:
Computing torque: τ = kp(θd-θ) + kd(θd-θ)
Translate it into current value I = K τ
BB:
Philosophy behind feedback control
Linear systems introduction – gains in linear control

## Slide 9
Statics of a quadruped robot
Triangle of support:
Movie of old controller making the dog walk on a rough terrain
9 unknown force components
6 equations of static equilibrium
→ Force indeterminate system!
- What are the forces then??
(BB)‏
Take moment of forces about this axis
BB:
Leg compliances
Helicoidal vector field

## Slide 10
Coordinate Systems and
Foot workspaces
Global Frame
Body Fixed
Frame
Workspace of a leg in body fixed frame
Leg workspaces are fixed in the body fixed frame
Homogeneous transformation matrix
Homogeneous coordinates:
BB:
Orthogonal and Rotation (SO) matrices – 2D and 3D
Euler angles, exponential coordinates (Euler's rotation theorem)‏
Worskpace boundary of littledog's legs (sphere) [refer to slide 2]

## Slide 11
Planning and Control Strategy
Generate a very rough trajectory for center of mass that needs to be followed (Planning)‏
Determine the direction in which the robot needs to move
Choose a new foothold that will make the robot move in the desired direction and make sure we choose a good foothold (greedy part of the algorithm)‏
Move body to triangle of support (actuation)‏
Update robot's body position from mocap readings (feedback)‏
Pick up leg and place it in the location chosen in step 3 (actuation)‏
Update robot's body position from mocap readings (feedback) [Repeat steps 2 to 7 until goal is reached]
Strategy I – A Greedy algorithm:
Strategy II – More elaborate planning of footholds:
Depending on the terrain do an elaborate planning of footholds.
Once we know the footholds that we need to follow, we just execute the corresponding body and foot motions to follow those footholds
Advantages: a. More optimal planning possible b. Since the footholds are known before execution is started, it is possible to have more efficient body pose control
c. Simultaneous body and foot motion
BB:
Details of algorithm
Terrain scores, segmentation
Body pose computation

## Slide 12
Dynamic gaits of the Littledog robot
Dynamic leap Movie
BB:
Impulsive torque
Optimization through simulation (paper)‏