## Slide 1: Cooperative Control of Autonomous Surface Vehicles for Oil Skimming and Cleanup
Hordur Heidarsson
Gaurav S. Sukhatme
Robotic Embedded Systems Laboratory
University of Southern California
Subhrajit Bhattacharya
Vijay Kumar
GRASP Laboratory
University of Pennsylvania

## Slide 2: Motivation
April 20, 2010: Deepwater Horizon drilling rig explosion, Gulf of Mexico
104 m3 of crude oil released into the ocean
Manual skimming operations at the surface removed ~3% of the oil – highly inefficient!
Our aim:
Develop an efficient automated roboticized skimming operation using Autonomous Surface Vehicles (ASVs).

## Slide 3: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 4: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 5: Drag Model
v = the relative velocity between the water and the cylindrical segment.
for fresh water at 25ºC
≈
cV – to be determined from experimental data.

## Slide 6: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 7: Dynamics of Skimmer Modeled as a Continuous Rope
FBD of an infinitesimal element
Difficult to solve!!

## Slide 8: Dynamics of Skimmer – The Catenary Analogy
Simplifying assumptions:
Quasi-static or steady-state : Inertial forces << drag forces
cS = cV = c : Isotropic drag coefficient.
Equations describing shape of a Catenary!
Closed-form solution:
Simplified equations:

## Slide 9: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 10: Discrete Dynamic Model
An n-segment link connected by revolute joints
Generalized coordinates for Lagrange’s equations:
Comparison between the steady-state shape from dynamic simulation of discrete model with the catenary shape predicted by continuous model:

## Slide 11: Discrete Dynamic Model – Complete Dynamic Simulation with Force Control
Given inputs: Force profile that is being applied by the towing boats (in red)

## Slide 12: Discrete Dynamic Model – Complete Dynamic Simulation with Position Control
Given inputs: Position of the towing boats (in red) as a function of time

## Slide 13: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 14: Discrete Quasi-static Model
Ignoring the inertia forces, the equations of motion become linear in the speeds:
where,
and
are functions of the shape variables
Control law for attaining a desired shape
current shape
gain matrix
Moore-Penrose pseudo-inverse
Note: A is nx4 matrix.
→ No full controllability for n>4
Boat speeds

## Slide 15: Discrete Quasi-static Model – Shape Control
n = 4, hence full controllability
Straight line → U-shape → V-shape → square enclosure
5x

## Slide 16: Discrete Quasi-static Model – Shape Control
n = 10, hence no full controllability
Desired shape: A circle
Failed to achieve desired shape!!

## Slide 17: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 18: Field Experiments
ASVs with on-board Mini-ITX 2 GHz dual-core computer
uBlox EKF-5H GPS for global positioning update @ 2 Hz
Microstrain 3D-M IMU with integrated compass sampled @ 50 Hz
ROS software platform
A 60 ft hollow diamond-braided polypropylene rope with ¾ in diameter to simulate the oil skimmer.
Microsoft LifeCam Cinema USB video camera for detecting the rope.
ASVs were manually driven at linear speed v and an initial separation distance D between them.
Echo Park Lake, Los Angeles

## Slide 19: Field Experiments – validation with shape predicted by quasi-static dynamic model
Recall: Shape predicted by quasi-static or steady-state dynamic model under assumption of cS = cV = c was the shape of a catenary.
Experimental data matches catenary shape
i.e., cS = cV = c
Thus, cV = cS = 0.05
From fluid mechanics
Experimentally estimated parameter

## Slide 20: Outline
Drag force model
Continuous dynamic model
Discrete dynamic model
  Simulated complete dynamic systems
Quasi-static model
  Shape control
Field experiments
Coverage maximization

## Slide 21: Coverage Maximization
Constraint: There is an upper limit to amount of net force that each boat can apply
Net force applied by each boat increases as the separation between them increase.
Data from simulation of full discrete dynamic model when the boats reach steady-state

## Slide 22: Coverage Maximization
But the drag force, hence the speed of the boats, depend on the net force that the boats apply.
(speed of boats decrease with the drag force)
– Attains maximum when separation is ~80% of rope length.
Φ(area swet per unit time) =
speed x separation

## Slide 23: Conclusion
We have derived from first principles the PDEs that govern the dynamics of a flexible rope being pulled by two ASVs on the water surface.
Proposed a discrete model and derived a numerical solution for it.
Experimentally validated the model under certain special cases and derived a parameter for the model experimentally.
Proposed a control law for controlling the shape of the discrete model under quasi-static assumptions.
We derived the condition under which the coverage rate is maximized - an important capability for efficient skimming operations.

## Slide 24: Acknowledgements
We gratefully acknowledge support from the ONR Antidote MURI project, grant no. N00014-09-1-1031. SB and VK acknowledge support from ONR Grant N00014-08-1-0696 and NSF Grant IIP-0742304. HH and GS were supported in part by the NOAA MERHAB program (NA05NOS4781228), NSF as part of the Center for Embedded Network Sensing (CENS) (CCR-0120778) and the ONR SoA program.
Thank you!
Questions?